## Slide 1
2022 Q1
Top 10 Bottlenecks
Quarterly Congestion Analysis Report
For the Baltimore, MD region
RITIS Performance Report

## Slide 2
Rank | Location | Previous Quarter Ranking | Avg. Max. Length (mi) | Avg. Daily Duration | Agency-reported Events | Base Impact
1 | MD-295 S @ MD 198 | 2 | 2.86 | 2h 19m | 224 | 33,466
2 | I-695 CW @ MD-122/SECURITY BLVD/EXIT 17 | -- | 2.33 | 1h 40m | 249 | 14,706
3 | I-95 S @ MD-43/WHITE MARSH BLVD/EXIT 67 | 7 | 7.56 | 26m | 213 | 16,300
4 | I-695 CW @ MD-372/WILKENS AVE/EXIT 12 | -- | 1.93 | 1h 2m | 409 | 9,928
5 | US-50 E @ WILLIAM PRESTON LANE BRG | -- | 4.42 | 52m | 817 | 19,281
6 | I-695 CCW @ I-83/MD-25/EXIT 23 | 9 | 3.38 | 39m | 318 | 9,997
7 | I-695 CCW @ US-40/EXIT 15 | 10 | 4.06 | 25m | 663 | 8,369
8 | I-95 N @ MD-152/EXIT 74 | 3 | 7.62 | 18m | 325 | 11,676
9 | I-695 CCW @ MD-26/EXIT 18 | -- | 2.09 | 46m | 303 | 7,934
10 | MD-295 S @ P.G./ANNE ARUNDEL CO LINE | -- | 4.21 | 30m | 244 | 10,291
Top 10 Bottlenecks in the Region
Bottlenecks are ranked by Base Impact – the sum of queue lengths over the duration of the bottleneck and weighted by speed differential, congestion or total delay (by default, the table is sorted by the base impact weighted by the total delay).
CW = Clockwise CCW = Counterclockwise
Red #s = highest value for that metric
Q1 2022

## Slide 3
For animated playback of corridor speeds
over time, click anywhere on the map below.
Corridor Speeds Over Time
MD-295 SB @ MD-198
Southbound PM congestion from MD 198 extending into the southern portion of the Baltimore region near Fort Meade occurring during both the morning and afternoon peak periods.
Volume-related delays are most likely caused by factors such as Baltimore commuters to DC and Fort Meade and the MD 295 merge with the heavily congested Capital Beltway.
1
Q1 2022
Quarterly Bottleneck Evaluation Summary
PK. AVG. SPEED
AM Peak | 7:50 AM
52.6 mph
(24% slower than free flow)
PM Peak | 5:35 PM
43.1 mph
(34% slower than free flow)
PK. TRAVEL TIME
AM Peak | 7:50 AM
17.1 min
PM Peak | 5:35 PM
20.8 min
Q1 DELAY COST
Delay Cost
$2.273M
Veh-hrs. of Delay
75,293 h
6AM – 8AM Arundel Mills Blvd. to MD-175
2PM – 6PM MD-175 to MD-198
Congested Locations
The center represents the beginning of 01.01.22 and the outer edge the end of 03.31.22
Bottleneck Occurrences
Most bottlenecks occurred between
2-7 PM
A
B
A
B
Arundel Mills Blvd.
32
B
A
(there were 224 Agency-reported events during Q1 2022)
General areas of events/incidents
Congested Locations
A
B
2-4.9
> 8
5-7.9
<2
Max Queue Length (miles)
Speed (mph)
10
0
20
30
40
50
Speed (mph)
10
0
20
30
40
50
Fort
Meade

## Slide 4
Ed Stylc, Planner Analyst
Baltimore Metropolitan Council
Offices at McHenry Row
1500 Whetstone Way, Suite 300
Baltimore, MD 21230
410.732.0500 ext. 1031office | 443.562.9751 cell | estylc@baltometro.org
For more information, contact:

RITIS Performance Report